## Slide 1
Tacit Collusion in Electricity Markets
Multi-Agent PPO on a 5-Bus DC-OPF Network
Pranav Puranik | Advisor: Dr. Liu | March 2026

## Slide 2
Research Question
Can independent reinforcement learning agents learn to tacitly collude in a realistic electricity market with network constraints?
Calvano et al. (2021) showed Q-learning agents collude in simple Cournot markets
We extend this to: asymmetric firms, DC-OPF network, continuous actions, PPO
Key metric: normalized profit gain Δ = (π – π_C) / (π_M – π_C)
Δ = 0: competitive outcome | Δ = 1: joint monopoly | Δ > 0: collusion

## Slide 3
Market Setup: 5-Bus Network
5-bus DC network with PTDF line constraints
Firm 0: 2 plants (Node 1: 150 MW, Node 2: 50 MW)
Firm 1: 1 plant (Node 2: 100 MW)
Quadratic cost: mc·g + ½·qc·g² per plant
Linear inverse demand at each node
ISO clears market via DC-OPF each step
Benchmarks (computed once)
Metric | Competitive | Monopoly
Avg LMP | $23.49 | higher
F0 profit/step | π_C(F0) | π_M(F0)
F1 profit/step | π_C(F1) | π_M(F1)
Δ | 0.0 | 1.0

## Slide 4
PPO Agent Architecture
Independent PPO (IPPO): one agent per firm
Actor: MLP → Gaussian mean per plant
Learnable log-std for exploration
Sigmoid × capacity → MW dispatch
Critic: MLP → scalar V(s)
Shared Adam optimizer (lr = 3e-4)
Architecture: 2 hidden layers, 64 units, Tanh
Dimensions
Component | Firm 0 | Firm 1
Observation | 5 × H | 5 × H
Action (plants) | 2 | 1
Action range | [0,150]+[0,50] | [0,100]
Hidden layers | 64-64 | 64-64

## Slide 5
Training Pipeline
Concept | Meaning | Value
Step | One env.step (1 hour of dispatch) | ~110K to converge
Episode | 168 consecutive steps (1 week) | 168 steps
Rollout | Steps before one PPO update | 2,048 steps
PPO Update | GAE + clipped surrogate + value loss | After each rollout
Session | One seed → train → converge/stop | 50 per H
Max Timesteps | Safety cap per session | 5,000,000
Flow: Agents act → ISO clears (DC-OPF) → LMPs + profit → buffer stores transition → every 2048 steps: PPO update → repeat

## Slide 6
Convergence: Δ-Stability Criterion
Calvano (Q-learning): greedy action unchanged at all states for 100,000 consecutive periods
Our adaptation for continuous PPO actions:
After each PPO update, compute Δ for both firms from recent episode profits
If max |Δ_new – Δ_old| < 0.02 for all firms: increment stable_count
If stable_count ≥ 50 consecutive updates (~102K steps): declare converged
Why not MW-based?
Continuous policies always drift slightly in raw output (±0.1–2 MW per update)
Calvano's discrete argmax either flips or doesn't — binary check. Not possible with continuous actions.
Δ-stability checks the economic outcome directly: has the profit level settled?

## Slide 7
Results: H = 1 (50 sessions)
Metric | Firm 0 (large) | Firm 1 (small)
Final Δ (mean ± std) | 0.441 ± 0.040 | 1.718 ± 0.092
Interpretation | 44% of collusion gap | Free-rides above monopoly share
Convergence step | ~110K ± 10.5K | ~110K ± 10.5K
Converged? | All 50 sessions | All 50 sessions
Key Findings
Both firms earn above competitive profits (Δ > 0) → tacit collusion emerges
Firm 0 (larger, 200 MW) restricts output → bears the cost of restraint
Firm 1 (smaller, 100 MW) free-rides on higher prices → Δ > 1
Consistent with asymmetric Cournot theory: smaller firms benefit disproportionately

## Slide 8
Comparison with Calvano et al. (2021)
Aspect | Calvano | Our Work
Algorithm | Q-learning (tabular) | PPO (neural network)
Action space | 15 discrete levels | Continuous [0, cap] MW
Firms | 2 symmetric | 2 asymmetric (different costs, caps)
Network | Single node, no constraints | 5-bus DC-OPF with line limits
Monitoring | Imperfect (stochastic demand) | Imperfect (LMP history only)
Convergence | Argmax unchanged 100K periods | Δ-stable for 50 updates (~102K steps)
Sessions | 1,000 | 50
Δ result | ~0.76 (symmetric) | F0: 0.44, F1: 1.72 (asymmetric)

## Slide 9
Next Steps
H = 2 and H = 3 jobs queued on Gilbreth (running next)
Does longer memory enable better punishment strategies?
Calvano found H=2 similar, H=3 slightly lower Δ (bigger state space hinders learning)
Analyze limit strategies and impulse responses across sessions
Does the average strategy show Calvano-style decreasing output vs. price?
Investigate the asymmetry: why Δ(F1) >> 1
Compare with Nash-Cournot equilibrium
Robustness: vary number of PPO epochs, learning rate, episode length